## Slide 1
AEROTHON 2026 - HAL x IITI
Team Name: Aerothona
Participants: Sudais Farooq

## Slide 2
Real-Time Four-Stage Turbojet Subsystem Health Estimation
PROBLEM UNDERSTANDING & MOTIVATION
• Goal: Monitor the state of a single-spool four-stage turbojet engine by estimating hidden component health indicators (Compressor, Combustor, Turbine health) and overall engine performance (Thrust, TSFC).
• Motivation: Direct physical measurement of turbine inlet temperature (T3) and interior component state is impossible in real-time due to extreme heat and aerodynamic pressure.
• Solution Significance: Real-time health estimation prevents catastrophic engine failures, reduces maintenance downtime, and optimizes fuel consumption.
• Challenge Scope: Flight envelope covers altitudes up to 12,053 m and speed up to 0.90 Mach. Rotor spool speeds run up to 80,941 RPM. Subsystem states degrade progressively over 30 cycles.
Page 1

## Slide 3
LITERATURE REVIEW / EXISTING APPROACHES
Page 2
Empirical Models vs. Physics-Informed Digital Twins
• Traditional Data-Driven Models: Standard Machine Learning models (MLP, XGBoost) fit telemetry data but ignore physical laws. They are prone to predicting non-physical engine states under flight envelope transitions.
• Constant Specific Heat Ratio Assumptions: Conventional textbook Thermodynamic models assume constant Specific Heat (gamma = 1.4), which fails above 1,000 K where air behaves as a calorically semi-perfect gas.
• High-Fidelity Simulation Models: Standard gas turbine transient simulation tools are highly accurate but computationally heavy, preventing real-time on-board edge diagnostics.
• Selected Framework: A Physics-Informed Neural Network (PINN) that integrates temperature-dependent gas dynamics (Cp(T) polynomials) to combine data-driven speed with thermodynamic consistency.

## Slide 4
PROPOSED METHODOLOGY & TECHNICAL APPROACH
Page 3
Grey-Box Physics-Informed Neural Network (PINN)
• Deep Learning Architecture: Multi-Layer Perceptron (MLP) mapping 13 inputs (sensors + Cycle) to 6 outputs (Health indexes, Thrust, TSFC).
• Calorically Semi-Perfect Gas Model: Evaluates specific heat ratio k(T) = R/Cp(T) dynamically at average compressor and turbine stage temperatures:
Cp(T) = 1005 + 0.05 * T + 1.5e-4 * T^2 - 8e-8 * T^3 J/(kg.K)
• Physics-Regularized Loss: Enforces isentropic compressor temperature rises, isentropic turbine work extraction, and combustor pressure recovery ratio (P3/P2 = 0.949).
• Multi-Objective Optimization: Formulates loss as a combination of data loss, empirical health checks, and Brayton cycle constraints.

## Slide 5
DATA SOURCES & PREPROCESSING
Page 4
Telemetry Scaling & Dataset Analysis
• Data Source: HAL PS-2 synthetic flight telemetry dataset. Consists of 10 virtual engine fleets operating over 30 cycles.
• Feature Engineering: Prepend Cycle (index 0) as the 13th feature to represent temporal wear progression.
• Scaling: Applied Standard Scaling to center inputs (X_mean, X_scale) and targets (y_mean, y_scale) around zero, ensuring balanced backpropagation gradient flow.
• Physics Unscaling: Scaling parameters are registered as PyTorch tensors to dynamically unscale parameters inside the custom loss module, allowing accurate physical laws evaluation.

## Slide 6
MODEL ARCHITECTURE / IMPLEMENTATION PLAN
Page 5
Model Export & Serverless Client-Side Deployment
• Training: Trained in PyTorch over 800 epochs with Adam optimizer and Cosine Annealing learning rate schedule.
• Model Conversion: Extracted weights, biases, and scaling factors from PyTorch .pt file and exported them to JavaScript (weights.js).
• Client-Side Execution: Neural network forward pass is computed directly in the user's browser using local matrix multiplication and Tanh activations.
• Hosting Strategy: 100% serverless, zero-config static site hosted on Netlify, requiring no backend python execution or database connections.

## Slide 7
EXPECTED OUTCOMES & EVALUATION METRICS
Page 6
Model Performance & Uncertainty Quantification (UQ)
• Performance Metrics on Test Set:
- CompressorHealth R2: 93.27% | CombustorHealth R2: 65.58% | TurbineHealth R2: 73.44%
- OverallHealth R2: 95.15% | Thrust R2: 99.13% | TSFC R2: 99.25%
• Uncertainty Bounds (95% Confidence Interval from 1.96 * Validation RMSE):
- Thrust: +/- 2,895 N | TSFC: +/- 0.0012 g/N/s
- Compressor: +/- 3.8% | Combustor: +/- 3.4% | Turbine: +/- 4.8% | Overall: +/- 2.2%
• Dashboard Visualization: Dynamic progress dials displaying prediction outputs alongside confidence intervals.

## Slide 8
TEAM COMPOSITION & CONTRIBUTIONS
Page 7
Roles and Responsibilities
• Sudais Farooq - Project Lead & Core Engineer: Developed the PyTorch PINN model, implemented the calorically semi-perfect gas thermodynamics loss functions, and compiled the training pipeline.
• Front-End Developer: Designed the widescreen HUD-themed glassmorphism dashboard, and implemented the browser-based matrix multiplier model runner.
• QA / System Deployer: Configured the local Express server, and prepared the Netlify static hosting deployment configurations.

## Slide 9
APPENDIX & REFERENCES
References & Documentation
• Reference 1: Challenge specifications and flight envelopes defined in HAL-IIT Indore Hackathon Problem Statement 2 (PS 2) pages.
• Reference 2: Hill, P. G., & Peterson, C. R., 'Mechanics and Thermodynamics of Propulsion', 2nd Edition.
• Project Repository: https://github.com/SudaisFarooq/Aerothon
• Live Web Application URL: https://github.com/SudaisFarooq/Aerothon