## Slide 1
AEROTHONA
Physics-Informed Digital Twin for Turbojet Diagnostics
Widescreen Technical Presentation | HAL Aerothon Submission

## Slide 2
01. The Challenge: Subsystem Health Monitoring
Hidden Subsystem Degradations
• Critical parameters (Compressor, Combustor, and Turbine health) cannot be directly measured via physical sensors due to extreme temperatures.
• Harsh operating envelopes cause progressive thermal and structural wear over multiple flight cycles.
• Traditional monitoring relies on delayed visual inspections and offline simulation models.
• Required: A real-time, interpretable system to estimate hidden health indicators, thrust output, and TSFC.
Dataset Physical Scope
→ Telemetry Input: 12 physical sensors + Cycle count (13 total features).
→ Flight Envelope: Continuous profile (Altitude: 0 to 12,053 m | Mach: 0.0 to 0.90).
→ Rotational Spool Speed: High-speed micro-turbojet configuration (30,120 to 80,941 RPM).
→ Cycle wear: Telemetry mapped from Cycle 1 to 30 to capture aging.

## Slide 3
02. Grey-Box Physics-Informed Neural Network
Deep Learning Backbone & Scaling
• Multi-Layer Perceptron (MLP) architecture: 13 inputs (sensors + cycle) -> Dense(64, Tanh) -> Dense(64, Tanh) -> Dense(32, Tanh) -> Dense(6, Linear) mapping outputs.
• Tanh activation functions enforce continuous second-order derivatives, ensuring smooth backpropagation gradients.
• Standard scaling maps inputs/outputs to standard normal distributions during backpropagation to prevent scale imbalances.
Calorically Semi-Perfect Thermodynamics
→ Temperature-Dependent Specific Heat: Discards constant cp assumptions (gamma=1.4) to calculate average cp dynamically based on temperature, capturing real gas behavior.
→ Compressor regularizations enforce isentropic compression efficiency bounds from inlet to Station 2.
→ Turbine regularizations enforce work extraction efficiency constraints from Station 3 to Station 4.
→ Empirical constraints: Combustor pressure drop ratio (P3/P2 = 0.949) and algebraic health sum (0.4*Comp + 0.3*Comb + 0.3*Turb = Overall).

## Slide 4
03. Model Accuracy & Uncertainty Quantification
Diagnostic Target | Validation RMSE | Test set R² Score
CompressorHealth | 0.0195 | 93.27%
CombustorHealth | 0.0174 | 65.58%
TurbineHealth | 0.0247 | 73.44%
OverallHealth | 0.0113 | 95.15%
Engine Thrust (N) | 1,476.80 N | 99.13%
TSFC (g/N/s) | 0.0006 | 99.25%
95% Confidence Intervals
• Uncertainty Bounds: Computed dynamically for predictions using 1.96 * Validation RMSE.
• Thrust Uncertainty: +/- 2,895 N (high accuracy, R²: 99.13%).
• TSFC Uncertainty: +/- 0.0012 g/N/s (R²: 99.25%).
• Component health bounds: Compressor (+/- 3.8%), Combustor (+/- 3.4%), Turbine (+/- 4.8%), Overall (+/- 2.2%).
• The 95% Confidence Interval is dynamically rendered beneath all performance values on the interface.

## Slide 5
04. Serverless Dashboard & Deployment
100% Client-Side Execution
• Model weights and standard scaling parameters are compiled directly into public/weights.js.
• Inference is computed instantly in browser javascript via matrix multiplications and tanh evaluations.
• No server round-trip network delays: predictions are generated instantly as sliders are moved.
• Removes backend database and server dependencies, allowing the web app to run offline or on any static host.
Hosting & Delivery Settings
→ GitHub Sync: Project code is committed and pushed directly to SudaisFarooq/Aerothon.
→ Netlify Support: Configured via netlify.toml, serving the public/ static assets folder automatically.
→ Zero Setup Deployment: Simply link the GitHub repo to Netlify to host it live for free in under 30 seconds.
→ Local Dev Server: Includes server.js to run on http://localhost:3000 if a local Express server is preferred.